## Slide 1: WAPP GEF Final results presentation
West African Power Pool (WAPP)
Grid Emission Factor (GEF) proposed as a Standardized Baseline
Cotonou
2-3 December 2014
Alexandre Dunod
Ecosur Afrique
Notes: Background:
The Standardised Baseline (SBL) provides the values of the CO2 emission factors for the interconnected electricity system of the WAPP and it is applicable to the group of countries connected to the WAPP. The SBL in the context of renewable energy and energy efficiency carbon projects is a vital tool towards reduction of transaction costs and improving the project implementation pace.

## Slide 2: Content
Summary of June 2014 meeting outcomes
    Main presentation topics
    Main discussion topics (Q&A)
    Main clarifications made to final report
Step-wise application of the Tool For Calculating GEF for an electricity system
  Identify the relevant electricity systems;
  Choose whether to include off-grid power plants in the project electricity system;
  Select a method to determine the operating margin (OM);
  Calculate the operating margin emission factor according to the selected method;
  Calculate the build margin (BM) emission factor;
  Calculate the combined margin (CM) emission factor.
Final Calculated Values for National and Regional GEFs
Conclusion and recommendations
Possible Next Steps - Action Plan

## Slide 3: Summary of June 2014 meeting
Main presentation topics:
WAPP background (states, network connections, imports and exports)
Grid Emission Factor introduction (rationale and methodology)
WAPP grid features (transmission constraintes, off-grid)
WAPP GEF data (requirements, state of country availability)
Benefits of GEF SBL, national vs. regional trade-offs
Typical regional GEF (SAPP example)
CDM presentation by Kusum Lata (UNFCCC), outline for capacity building

## Slide 4: Summary of June 2014 meeting (continued)
Main discussion topics (Q&A):
Undistributed energy (off-grid, suppressed demand, transmission losses)
Data availability, IPP inclusion, secondary networks
Trans-border imports/exports, multi-country power production allocation
Togo / Benin differentiation
DNA and other ongoing GEF calculations
Higher vs. lower GEF values preferences (Baseline or Project Emissions), quantitative trade-offs
transmission constraints vs. synchronisation issues; methodological latitude/flexibility
Operation Margin calculation, Build Margin most recent units selection and Combined Margin standard weighting
Validity duration of the GEF, carbon market value and perspectives
ownership and distribution of future WAPP emission reduction benefits
outline on capacity building and DNA awareness

## Slide 5: Summary of June 2014 meeting (continued)
Main clarifications made to final report:
Comments on draft report received from TCN, VRA, GridCo, CIE & WAPP
Explanations on all confusing matters from Q&A (minutes)
Clarifications on SBL procedure and existing guidelines
p.8 Fig 4 (IRENA imports scenario) – prospective differentiated from WAPP master plan
p.9 Tab 2 (IRENA capacity additions scenario) – meaning of decentralized; IPP vs. off-grid
Net vs. growth power generation accounting
p.15 Fig 8: Burkina Faso – Niger connection (North corridor project)
p.41 Benin & Togo installed capacities differentiated
References to respective data sources (WAPP members / WAPP reports / IRENA / GIZ economic outlooks etc.)
Various editorial corrections and improvements

## Slide 6: GEF Methodological tool (UNFCCC)
Step 1: Identifying the relevant electricity systems;
Step 2: Choose whether to include off-grid power plants in the project electricity system;
Step 3: Select a method to determine the operating margin (OM);
Step 4: Calculate the operating margin emission factor according to the selected method;
Step 5: Calculate the build margin (BM) emission factor;
Step 6: Calculating the combined margin (CM) emission factor.
“Tool to calculate the emission factor for an electricity system” (v 4.0.0)

## Slide 7: Step 1: Identify the relevant electricity systems
Notes: Simplified map of WAPP members and their interconnected transmission lines

## Slide 8: Step 1 (continued) - WAPP electricity market (GWh)
Chart: 
| Benin/ Togo | Niger | Mali | Burkina Faso | Senegal | Ghana | Cote d'Ivoire | Nigeria | Gambia | Guinea | Guinea Bissau | Sierra Leone | Liberia
2013 Import | 1935 | 602 | 596.6 | 481.816 | 308.4923 | 120 | 32.1 | 0 | 0 | 0 | 0 | 0 | 0
2012 Import | 1812 | 641 | 13 | 472 | 290 | 177 | 54 | 0 | 0 | 0 | 0 | 0 | 0
2011 Import | 1847 | 552 | 0 | 449 | 257 | 81 | 22 | 0 | 0 | 0 | 0 | 0 | 0
2013 Export | -2 | -4 | -212.6 | 0 | 0 | -653 | -825 | -1788.531 | 0 | 0 | 0 | 0 | 0
2012 Export | -2 | -4 | -471 | 0 | 0 | -675 | -658 | -1722 | 0 | 0 | 0 | 0 | 0
2011 Export | -1 | -2 | -419 | 0 | 0 | -698 | -615 | -1696 | 0 | 0 | 0 | 0 | 0
Notes: Information on existing transmission infrastructure is based on the WAPP Master Plan 2011, IRENA 2013 and data/information received from the WAPP Secretariat
It is noteworthy that some countries such as Liberia have limited power import to rural areas at the borders (e.g. from Côte d’Ivoire). These occur in isolated grids with no connection to the national power grids.

## Slide 9: Step 1 (continued) - Transmission constraints check
Notes: The actual trades (in MWh) were divided by the maximum operational capacities per transmission line (in MWh) to lead to current load factor per line. If the load factor for both directions was below 90%, it was concluded that there is no existing transmission constraint

## Slide 10: Step 2: Choose whether to include off-grid power plants in the project electricity system
Although off-grid diesel-based power generation in the WAPP region is significant, the options to include off-grid are:
II.a (Section 6.2.3): based on available data on off-grid power units in the country
OR II.b (Section 6.2.3): default 10% contribution for
LDCs/SIDS or countries with less than 10 registered CDM
projects (demonstration of load shedding program)
Hence, off-grid generation is excluded
 lack of necessary data
 Nigeria, Ghana and Côte d’Ivoire are not eligible

## Slide 11: Step 3: Select a method to determine the operating margin (OM)
Must-runs (hydro) generate 23,5% of total electricity
Years | 2009 | 2010 | 2011 | 2012 | 2013 | AVG
Total WAPP (MWh) | 31,246,756 | 36,338,337 | 38,501,818 | 42,256,048 | 14,347,665 | 32,538,125
Low cost/must run (MWh) | 9,930,618 | 9,323,535 | 8,742,084 | 8,498,497 | 1,774,859 | 7,653,919
Share of Low cost/must run (%) | 31.78% | 25.66% | 22.71% | 20.11% | 12.37% | 23.52%
5yr average Low cost / must run: | 23.52% | Simple OM Possible? |  | YES |  | 
 Simple Operating Margin calculation is applicable
Notes: (a) Simple OM; or
(b) Simple adjusted OM; or
(c) Dispatch data analysis OM; or
(d) Average OM.
The Simple OM method can only be used if low-cost/must-run resources constitute less than 50% of total grid generation (excluding off-grid power plants) in the five most recent years (2009-2013).

## Slide 12: Step 3 (continued) – data collection requirements
Information to clearly identify the plant;
Date of commissioning;
Capacity (MW);
Fuel type(s) used;
Net electricity generation in the relevant year(s)
Fuel consumption of each fuel type in the relevant year(s)
Load curves (if available)
Fuel specifications (NCV & EF, or IPCC default)
Imports/exports records
(a minimum of 5 years of historical data is needed)

## Slide 13: Step 3 (continued) - Possible data vintages:
Ex-ante: 3-year generation-weighted average by using the most recent data available at the time of validation; no need for monitoring and recalculating the emission factor during the crediting period.
Ex-post: updated for the year in which the power plant displaces grid electricity; emission factor should be recalculated annually
 ex-ante approach is selected (2010-2012 data), valid for the duration of the Standardized baseline
Notes: Nigeria missing data following liberalization
SBL 3 years ?

## Slide 14: Step 4: Calculate the operating margin emission factor according to the selected method
Generation-weighted average CO2 emissions per unit of net electricity generation (tCO2/MWh), excluding LC/MR
Where
EFgrid,OM simple,y | = Simple operating margin CO2 emission factor in year y (tCO2/MWh)
EGm,y | = Net quantity of electricity generated & delivered to the grid by power unit m in year y (MWh)
EFEL,m,y | = CO2 emission factor of power unit m in year y (tCO2/MWh)
m | = All power units serving the grid in year y except low-cost/must-run power units
y | = The relevant year as per the data vintage chosen in Step 3
Notes: not including low-cost/must-run power plants/units

## Slide 15: Step 4 (continued) – Determination of FEEL,m,y
Option A1: If data on fuel consumption and electricity generation is available, the emission factor is determined as
Where
FCi,m,y | = Amount of fuel type i consumed by power unit m in year y (Mass or volume unit)
NCVi,y | = Net calorific value (energy content) of fuel type i in year y (GJ/mass or volume unit)
EFCO2,I,y | = CO2 emission factor of fuel type i in yea y (tCO2/GJ)
EGm,y | = Net quantity of electricity generated and delivered to the grid by power unit m in year y (MWh)
i | = All fuel types combusted in power unit m in year y

## Slide 16: Step 4 (continued) – Determination of FEEL,m,y
Option A2: If only data on electricity generation and the fuel types used is available, determination based on the CO2 emission factor of the fuel type used and the efficiency of the power unit, as
Where
EFCO2,m,I,y | = Average CO­2 emission factor of fuel type i used in power unit m in year y (tCO2/GJ)
Ƞm,y | = Average net energy conversion efficiency of power unit m in year y (ratio)
i | = All fuel types combusted in power unit m in year y

## Slide 17: Step 4 (continued) – WAPP OM calculation results

## Slide 18: Step 5: Calculate the build margin (BM) emission factor

## Slide 19: Step 5 (continued) - WAPP BM calculation results
5 most recent units as of 2012: Niger AGGREKO GOUDEL, Nigeria OMOTOSH NIPP, Burkina Faso Komsilga, Nigeria SAPELE NIPP, Senegal Location APR
20% of power generation encompasses more (16 units)
Total ∑EG without CDM (MWh) | 13,069,865 | 
Criteria | SET 5 units | SET 20%
Total Power generation for BM (MWh) | 808,710 | 3,140,867
Emissions for BM (tCO2) | 518,530 | 1,996,599
Build Margin excl. off-grid | 0.6412 | 0.6357
Selected BM for the WAPP (tCO2/MWh) | 0.6357 | 

## Slide 20: Step 6: Calculate the combined margin (CM) emission factor
For wind and solar power generation projects, wOM = 0.75, wBM = 0.25 for all crediting periods
For all other projects, wOM = 0.5, wBM = 0.5 for the first crediting period, and wOM = 0.25, wBM = 0.75 for second and third crediting period

## Slide 21: Step 6 (continued) – WAPP GEF results
Project types | 1st crediting period |  |  |  |  | 2nd or 3rd crediting period |  |  |  | 
 | OM | BM | CM | Wom | Wbm | OM | BM | CM | Wom | Wbm
Solar and Wind power project | 0.5715 | 0.6357 | 0.588 | 0.75 | 0.25 | 0.5715 | 0.6357 | 0.588 | 0.75 | 0.25
Other renewables | 0.5715 | 0.6357 | 0.604 | 0.5 | 0.5 | 0.5715 | 0.6357 | 0.62 | 0.25 | 0.75
Other projects | 0.5715 | 0.6357 | 0.604 | 0.5 | 0.5 | 0.5715 | 0.6357 | 0.62 | 0.25 | 0.75
 Applicable WAPP GEF values range between 0.59 to 0.62 tCO2/MWh

## Slide 22: National and regional GEFs
WAPP member | Latest GEF in tCO2/MWh (year) | Newly calculated GEF
Senegal | 0.67 (2008) | 0.59 (WAPP 2012)
Cote d’Ivoire | 0.65 (2013) | 
Nigeria | 0.59 (2008) | 
Mali | 0.58 (2006) | 
Togo & Benin | 0.41 (2011) | 
Ghana | 0.38 (2010) | 
Burkina Faso | - | 
Niger | - | 
Gambia | 0.72 (2012) | 0.59
Guinea | 0.49 (2008) | 0.32
Sierra Leone | 0.40 (2010) | 0.23
Guinea Bissau | - | 0.67
Liberia | - | 0.59
Yellow means WAPP-disconnected

## Slide 23: Thank you for your attention
Alexandre Dunod
a.dunod@ecosurafrique.com
Tel: +230 59 84 56 49